## Slide 1: ENGINEERING CURVES Part- I {Conic Sections}
ELLIPSE
1.Concentric Circle Method
2.Rectangle Method
3.Oblong Method
4.Arcs of Circle Method
5.Rhombus Metho
6.Basic Locus Method (Directrix – focus)
HYPERBOLA
1.Rectangular Hyperbola
(coordinates given)
2 Rectangular Hyperbola
(P-V diagram - Equation given)
3.Basic Locus Method (Directrix – focus)
PARABOLA
1.Rectangle Method
2 Method of Tangents ( Triangle Method)
3.Basic Locus Method (Directrix – focus)
Methods of Drawing Tangents & Normals To These Curves.

## Slide 2
Section Plane Through Generators
Ellipse
Section Plane Parallel to end generator.
Section Plane
Parallel to Axis.
Hyperbola
CONIC SECTIONS
ELLIPSE, PARABOLA AND HYPERBOLA ARE CALLED CONIC SECTIONS
BECAUSE
THESE CURVES APPEAR ON THE SURFACE OF A CONE WHEN IT IS CUT BY SOME TYPICAL CUTTING PLANES.
OBSERVE ILLUSTRATIONS GIVEN BELOW..

## Slide 3
For Ellipse E<1
For Parabola E=1 C)
For Hyperbola E>1
Refer Problem nos. 6. 9 & 12
SECOND DEFINATION OF AN ELLIPSE:-
It is a locus of a point moving in a plane
such that the SUM of it’s distances from TWO fixed points
always remains constant.
{And this sum equals to the length of major axis.} These TWO fixed points are FOCUS 1 & FOCUS 2
Refer Problem no.4
Ellipse by Arcs of Circles Method.
COMMON DEFINATION OF ELLIPSE, PARABOLA & HYPERBOLA:
These are the loci of points moving in a plane such that the ratio of it’s distances from a fixed point And a fixed line always remains constant.
The Ratio is called ECCENTRICITY. (E)

## Slide 4: ELLIPSE BY CONCENTRIC CIRCLE METHOD
1
2
3
4
5
6
7
8
9
10
B
A
C
1
2
3
4
5
6
7
8
D
9
10
Steps:
Draw both axes as perpendicular bisectors of each other & name their ends as shown.
Taking their intersecting point as a center, draw two concentric circles considering both as respective diameters.
Divide both circles in 12 equal parts & name as shown.
From all points of outer circle draw vertical lines downwards and upwards respectively.
5.From all points of inner circle draw
horizontal lines to intersect those vertical lines.
Mark all intersecting points properly as those are the points on ellipse.
Join all these points along with the ends of both axes in smooth possible curve. It is required ellipse.
Problem 1 :-
Draw ellipse by concentric circle method.
Take major axis 100 mm and minor axis 70 mm long.

## Slide 5: ELLIPSE BY RECTANGLE METHOD
1
2
3
4
1
2
3
4
A
B
C
D
Problem 2
Draw ellipse by Rectangle method.
Take major axis 100 mm and minor axis 70 mm long.
Steps:
1 Draw a rectangle taking major and minor axes as sides.
In this rectangle draw both axes as perpendicular bisectors of each other..
For construction, select upper left part of rectangle. Divide vertical small side and horizontal long side into same number of equal parts.( here divided in four parts)
Name those as shown..
Now join all vertical points 1,2,3,4, to the upper end of minor axis. And all horizontal points i.e.1,2,3,4 to the lower end of minor axis.
Then extend C-1 line upto D-1 and mark that point. Similarly extend C-2, C-3, C-4 lines up to D-2, D-3, & D-4 lines.
Mark all these points properly and join all along with ends A and D in smooth possible curve. Do similar construction in right side part.along with lower half of the rectangle.Join all points in smooth curve.
It is required ellipse.

## Slide 6: ELLIPSE BY OBLONG METHOD
1
2
3
4
A
B
1
2
4
3
Problem 3:-
Draw ellipse by Oblong method.
Draw a parallelogram of 100 mm and 70 mm long sides with included angle of 750.Inscribe Ellipse in it.
STEPS ARE SIMILAR TO THE PREVIOUS CASE (RECTANGLE METHOD)
ONLY IN PLACE OF RECTANGLE,
HERE IS A PARALLELOGRAM.

## Slide 7: ELLIPSE BY ARCS OF CIRCLE METHOD
F1
F2
1 2 3 4
A
B
C
D
p
1
p2
p3
p4
O
PROBLEM 4.
MAJOR AXIS AB & MINOR AXIS CD ARE 100 AMD 70MM LONG RESPECTIVELY
.DRAW ELLIPSE BY ARCS OF CIRLES METHOD.
STEPS:
Draw both axes as usual.Name the ends & intersecting point
Taking AO distance I.e.half major axis, from C, mark F1 & F2 On AB . ( focus 1 and 2.)
On line F1- O taking any distance, mark points 1,2,3, & 4
Taking F1 center, with distance A-1 draw an arc above AB and taking F2 center, with B-1 distance cut this arc. Name the point p1
Repeat this step with same centers but taking now A-2 & B-2 distances for drawing arcs. Name the point p2 6.Similarly get all other P points.
With same steps positions of P can be located below AB.
7.Join all points by smooth curve to get an ellipse/
As per the definition Ellipse is locus of point P moving in a plane such that the SUM of it‟s distances from two fixed points (F1 & F2) remains constant and equals to the length of major axis AB.(Note A .1+ B .1=A . 2 + B. 2 = AB)

## Slide 8: ELLIPSE BY RHOMBUS METHOD
1
4
2
3
A
B
D
C
PROBLEM 5.
DRAW RHOMBUS OF 100 MM & 70 MM LONG DIAGONALS AND INSCRIBE AN ELLIPSE IN IT.
STEPS:
Draw rhombus of given
dimensions.
Mark mid points of all sides & name Those A,B,C,& D
Join these points to the ends of smaller diagonals.
Mark points 1,2,3,4 as four centers.
Taking 1 as center and 1-A
radius draw an arc AB.
Take 2 as center draw an arc CD.
Similarly taking 3 & 4 as centers and 3-D radius draw arcs DA & BC.

## Slide 9: ELLIPSE DIRECTRIX-FOCUS METHOD
PROBLEM 6:- POINT F IS 50 MM FROM A LINE AB.A POINT P IS MOVING IN A PLANE SUCH THAT THE RATIO OF IT’S DISTANCES FROM F AND LINE AB REMAINS CONSTANT AND EQUALS TO 2/3 DRAW LOCUS OF POINT P. { ECCENTRICITY = 2/3 }
F ( focus)
(vertex) V
ELLIPSE
A
B
STEPS:
.Draw a vertical line AB and point F 50 mm from it.
.Divide 50 mm distance in 5 parts.
.Name 2nd part from F as V. It is 20mm
and 30mm from F and AB line resp. It is first point giving ratio of it’s distances from F and AB 2/3 i.e 20/30
Form more points giving same ratio such as 30/45, 40/60, 50/75 etc.
Taking 45,60 and 75mm distances from line AB, draw three vertical lines to the right side of it.
Now with 30, 40 and 50mm distances in compass cut these lines above and below, with F as center.
Join these points through V in smooth curve.
This is required locus of P.It is an ELLIPSE.
45mm

## Slide 10: PARABOLA RECTANGLE METHOD
1
2
3
4
5
6
1
2
3 4 5
6
1
2
3
4
5
6
5
4
3 2 1
PROBLEM 7: A BALL THROWN IN AIR ATTAINS 100 M HIEGHT AND COVERS HORIZONTAL DISTANCE 150 M ON GROUND.
Draw the path of the ball (projectile)-
STEPS:
1.Draw rectangle of above size and divide it in two equal vertical parts 2.Consider left part for construction. Divide height and length in equal number of parts and name those 1,2,3,4,5& 6
Join vertical 1,2,3,4,5 & 6 to the top center of rectangle
Similarly draw upward vertical lines from horizontal1,2,3,4,5 And wherever these lines intersect previously drawn inclined lines in sequence Mark those points and
further join in smooth possible curve. 5.Repeat the construction on right side rectangle also.Join all in sequence.
This locus is Parabola.
.

## Slide 11: PARABOLA METHOD OF TANGENTS
C
A
B
Problem no.8: Draw an isosceles triangle of 100 mm long base and 110 mm long altitude.Inscribe a parabola in it by method of tangents.
Solution Steps:
Construct triangle as per the given
dimensions.
Divide it’s both sides in to same no.of equal parts.
Name the parts in ascending and descending manner, as shown.
4. Join 1-1, 2-2,3-3 and so on.
5. Draw the curve as shown i.e.tangent to all these lines. The above all lines being tangents to the curve, it is called method of tangents.

## Slide 12: PARABOLA DIRECTRIX-FOCUS METHOD
A
B
PARABOLA
(VERTEX) V
F
( focus)
1 2 3 4
SOLUTION STEPS:
Locate center of line, perpendicular to AB from point F. This will be initial point P and also the vertex.
Mark 5 mm distance to its right side, name those points 1,2,3,4 and from
those
draw lines parallel to AB.
Mark 5 mm distance to its left of P and name it 1.
Take O-1 distance as radius and F as center draw an arc
cutting first parallel line to AB. Name upper point P1 and lower point P2.
(FP1=O1)
Similarly repeat this process by taking again 5mm to right and left and locate P3P4.
Join all these points in smooth curve.
It will be the locus of P equidistance from line AB and fixed point F.
PROBLEM 9: Point F is 50 mm from a vertical straight line AB.
Draw locus of point P, moving in a plane such that
it always remains equidistant from point F and line AB.
O
P1
P2

## Slide 13: HYPERBOLA
P
O
40 mm
30 mm
1
2
3
2 1
1
2
3
1
2
THROUGH A POINT
OF KNOWN CO-ORDINATES
Solution Steps:
Extend horizontal line from P to right side.
Extend vertical line from P upward.
On horizontal line from P, mark some points taking any distance and name them after P-1, 2,3,4 etc.
Join 1-2-3-4 points to pole O. Let them cut part [P-B] also at 1,2,3,4 points.
From horizontal 1,2,3,4 draw vertical lines downwards and
From vertical 1,2,3,4 points [from P-B] draw
horizontal lines.
7) Line from 1 horizontal and line from 1 vertical will meet at
P1.Similarly mark P2, P3, P4 points.
8) Repeat the procedure by marking four points on upward vertical line from P and joining all those to pole O. Name this points P6, P7, P8 etc. and join them by smooth curve.
Problem No.10: Point P is 40 mm and 30 mm from horizontal and vertical axes respectively.Draw Hyperbola through it.

## Slide 14: HYPERBOLA P-V DIAGRAM
PRESSURE
( Kg/cm2)
0
1 2 3 4 5 6 7 8 9
VOLUME:( M3 )
10
10
9
8
7
6
5
4
3
2
1
Problem no.11: A sample of gas is expanded in a cylinder from 10 unit pressure to 1 unit pressure.Expansion follows law PV=Constant.If initial volume being 1 unit, draw the curve of expansion. Also Name the curve.
Form a table giving few more values of P & V
P | V = | C
10 | 1 = | 10
5 | 2 = | 10
4 | 2.5 = | 10
2.5 | 4 = | 10
2 | 5 = | 10
1 | 10 = | 10
Now draw a Graph of Pressure against Volume.
It is a PV Diagram and it is Hyperbola. Take pressure on vertical axis and Volume on horizontal axis.

## Slide 15: HYPERBOLA DIRECTRIX FOCUS METHOD
F ( focus)
V
(vertex)
A
B
30mm
PROBLEM 12:- POINT F IS 50 MM FROM A LINE AB.A POINT P IS MOVING IN A PLANE SUCH THAT THE RATIO OF IT’S DISTANCES FROM F AND LINE AB REMAINS CONSTANT AND EQUALS TO 2/3 DRAW LOCUS OF POINT P. { ECCENTRICITY = 2/3 }
STEPS:
.Draw a vertical line AB and point F 50 mm from it.
.Divide 50 mm distance in 5 parts.
.Name 2nd part from F as V. It is 20mm and 30mm from F and AB line resp.
It is first point giving ratio of it’s distances from F and AB 2/3 i.e 20/30
Form more points giving same ratio such as 30/45, 40/60, 50/75 etc.
Taking 45,60 and 75mm distances from line AB, draw three vertical lines to the right side of it.
Now with 30, 40 and 50mm distances in compass cut these lines above and below, with F as center.
Join these points through V in smooth curve.
This is required locus of P.It is an ELLIPSE.

## Slide 16
D
F1
F2
1 2 3 4
A
B
C
p1
p3
p2
p4
O
Q
TO THE CURVE FROM A GIVEN POINT ( Q )
JOIN POINT Q TO F1 & F2
BISECT ANGLE F1Q F2 THE ANGLE BISECTOR IS NORMAL
A PERPENDICULAR LINE DRAWN TO IT IS TANGENT TO THE CURVE.
ELLIPSE
TANGENT & NORMAL
TO DRAW TANGENT & NORMAL
Problem 13:

## Slide 17: ELLIPSE TANGENT & NORMAL
F ( focus)
ELLIPSE
(vertex) V
A
B
T
T
N
Q
N
900
TO DRAW TANGENT & NORMAL TO THE CURVE
FROM A GIVEN POINT ( Q )
JOIN POINT Q TO F.
CONSTRUCT 900 ANGLE WITH THIS LINE AT POINT F
EXTEND THE LINE TO MEET DIRECTRIX AT T
JOIN THIS POINT TO Q AND EXTEND. THIS IS TANGENT TO ELLIPSE FROM Q
TO THIS TANGENT DRAW PERPENDICULAR
LINE FROM Q. IT IS NORMAL TO CURVE.
Problem 14:

## Slide 18: PARABOLA TANGENT & NORMAL
A
B
PARABOLA
( focus)
VERTEX V F
Q
T
N
N
T
900
TO DRAW TANGENT & NORMAL
TO THE CURVE FROM A GIVEN POINT ( Q )
JOIN POINT Q TO F.
CONSTRUCT 900 ANGLE WITH THIS LINE AT POINT F
EXTEND THE LINE TO MEET DIRECTRIX AT T
JOIN THIS POINT TO Q AND EXTEND. THIS IS TANGENT TO THE CURVE FROM Q
TO THIS TANGENT DRAW PERPENDICULAR
LINE FROM Q. IT IS NORMAL TO CURVE.
Problem 15:

## Slide 19: HYPERBOLA TANGENT & NORMAL
F ( focus)
V
(vertex)
A
B
N Q
N
T
T
900
TO DRAW TANGENT & NORMAL
TO THE CURVE FROM A GIVEN POINT ( Q )
JOIN POINT Q TO F.
CONSTRUCT 900 ANGLE WITH THIS LINE AT POINT F
EXTEND THE LINE TO MEET DIRECTRIX AT T
JOIN THIS POINT TO Q AND EXTEND. THIS IS TANGENT TO CURVE FROM Q
TO THIS TANGENT DRAW PERPENDICULAR LINE FROM Q. IT IS NORMAL TO CURVE.
Problem 16

## Slide 20: CYCLOID
P
C1
C2
C3
C4
C5
C6
C7
C8
p1
p3
p4
p5
p6
p7
p8
1
2
3
4
5
6
7
C p2
D
PROBLEM 22: DRAW LOCUS OF A POINT ON THE PERIPHERY OF A CIRCLE
WHICH ROLLS ON STRAIGHT LINE PATH. Take Circle diameter as 50 mm
Solution Steps:
From center C draw a horizontal line equal to D distance.
Divide D distance into 8 number of equal parts and name them C1, C2, C3 etc.
Divide the circle also into 8 number of equal parts and in clock wise direction, after P name 1, 2, 3 up to 8.
From all these points on circle draw horizontal lines. (parallel to locus of C)
With a fixed distance C-P in compass, C1 as center, mark a point on horizontal line from 1. Name it P.
Repeat this procedure from C2, C3, C4 upto C8 as centers. Mark points P2, P3, P4, P5 up to P8 on the
horizontal lines drawn from 2, 3, 4, 5, 6, 7 respectively.
Join all these points by curve. It is Cycloid.

## Slide 21
C2
EPI CYCLOID :
P
O
r = CP
R
3600
= r
1
2
3
5
6
7
Generating/ Rolling Circle4
Directing Circle
PROBLEM 25: DRAW LOCUS OF A POINT ON THE PERIPHERY OF A CIRCLE
WHICH ROLLS ON A CURVED PATH. Take diameter of rolling Circle 50 mm And radius of directing circle i.e. curved path, 75 mm.
Solution Steps:
When smaller circle will roll on larger circle for one revolution it will cover  D distance on arc and it will be decided by included arc angle .
Calculate  by formula  = (r/R) x 3600.
Construct angle  with radius OC
and draw an arc by taking O as center OC as radius and form sector of angle
.
Divide this sector into 8 number of equal angular parts. And from C onward name them C1, C2, C3 up to C8.
Divide smaller circle (Generating circle) also in 8 number of equal parts. And next to P in clockwise direction name those 1, 2, 3, up to 8.
With O as center, O-1 as radius draw an arc in the sector. Take O-2, O- 3, O-4, O-5 up to O-8 distances with center O, draw all concentric arcs in sector. Take fixed distance C-P in compass, C1 center, cut arc of 1 at P1. Repeat procedure and locate P2, P3, P4, P5 unto P8 (as in cycloid) and join them by smooth curve. This is EPI – CYCLOID.

## Slide 22: HYPO CYCLOID
P1
P2
P
3
P
4
P
5
P6
P7
P8
P
1
2
3
6
5
7
4
O
OC = R ( Radius of Directing Circle) CP = r (Radius of Generating Circle)
r
3600
= R
PROBLEM 26: DRAW LOCUS OF A POINT ON THE PERIPHERY OF A CIRCLE WHICH ROLLS FROM THE INSIDE OF A CURVED PATH. Take diameter of
rolling circle 50 mm and radius of directing circle (curved path) 75 mm.
Solution Steps:
Smaller circle is rolling
here, inside the larger circle. It has to rotate anticlockwise to move ahead.
Same steps should be taken as in case of EPI – CYCLOID. Only change is in numbering direction of 8 number of equal parts on the smaller circle.
From next to P in anticlockwise direction, name 1,2,3,4,5,6,7,8.
Further all steps are that of epi – cycloid. This is called
HYPO – CYCLOID.

## Slide 23: CYCLOID Method of Drawing Tangent & Normal
N
STEPS:
DRAW CYCLOID AS USUAL.
MARK POINT Q ON IT AS DIRECTED.
WITH CP DISTANCE, FROM Q. CUT THE POINT ON LOCUS OF C AND JOIN IT TO Q.
FROM THIS POINT DROP A PERPENDICULAR ON GROUND LINE AND NAME IT N
JOIN N WITH Q.THIS WILL BE NORMAL TO
CYCLOID.
DRAW A LINE AT RIGHT ANGLE TO THIS LINE FROM Q.
IT WILL BE TANGENT TO CYCLOID.
P
C1
C2
C3
C4
C5
C6
C7
C8
CYCLOID
Q
D
C

## Slide 24: SCALES
FOR FULL SIZE SCALE R.F.=1 OR ( 1:1 ) MEANS DRAWING
& OBJECT ARE OF
SAME SIZE.
Other RFs are described as
1:10, 1:100,
1:1000, 1:1,00,000
DIMENSIONS OF LARGE OBJECTS MUST BE REDUCED TO ACCOMMODATE ON STANDARD SIZE DRAWING SHEET.THIS REDUCTION CREATES A SCALE OF THAT REDUCTION RATIO, WHICH IS GENERALLY A FRACTION..
SUCH A SCALE IS CALLED REDUCING SCALE AND
THAT RATIO IS CALLED REPRESENTATIVE FACTOR.
SIMILARLY IN CASE OF TINY OBJECTS DIMENSIONS MUST BE INCREASED FOR ABOVE PURPOSE. HENCE THIS SCALE IS CALLED ENLARGING SCALE. HERE THE RATIO CALLED REPRESENTATIVE FACTOR IS MORE THAN UNITY.
A
USE FOLLOWING FORMULAS FOR THE CALCULATIONS IN THIS TOPIC.
B LENGTH OF SCALE = R.F. X MAX. LENGTH TO BE MEASURED.
DIMENSION OF DRAWING
REPRESENTATIVE FACTOR (R.F.) =
DIMENSION OF OBJECT
= LENGTH OF DRAWING ACTUAL LENGTH
= AREA OF DRAWING
V ACTUAL AREA
= 3 VOLUME AS PER DRWG. V ACTUAL VOLUME

## Slide 25
( FOR DIMENSIONS UP TO SINGLE DECIMAL) ( FOR DIMENSIONS UP TO TWO DECIMALS)
( FOR DIMENSIONS UP TO TWO DECIMALS)
PLAIN SCALES
DIAGONAL SCALES
VERNIER SCALES
COMPARATIVE SCALES ( FOR COMPARING TWO DIFFERENT UNITS)
SCALE OF CORDS ( FOR MEASURING/CONSTRUCTING ANGLES)
TYPES OF SCALES:
= 10 METRES
= 10 DECIMETRES
= 10 CENTIMETRES
= 10 MILIMETRES
1 DECAMETRE
1 METRE
1 DECIMETRE
1 CENTIMETRE
BE FRIENDLY WITH THESE UNITS.
1 KILOMETRE = 10 HECTOMETRES
1 HECTOMETRE = 10 DECAMETRES

## Slide 26
0
4
5
METERS
10
DECIMETERS
4 M 6 DM
1 2 3
R.F. = 1/100
PLANE SCALE SHOWING METERS AND DECIMETERS.
PLAIN SCALE
PLAIN SCALE:-This type of scale represents two units or a unit and it‟s sub-division.
PROBLEM NO.1:- Draw a scale 1 cm = 1m to read decimeters, to measure maximum distance of 6 m.
Show on it a distance of 4 m and 6 dm.
CONSTRUCTION:-
a) Calculate R.F.=
R.F.= 1cm/ 1m = 1/100
Length of scale = R.F. X max. distance
= 1/100 X 600 cm
= 6 cms
Draw a line 6 cm long and divide it in 6 equal parts. Each part will represent larger division unit.
Sub divide the first part which will represent second unit or fraction of first unit.
Place ( 0 ) at the end of first unit. Number the units on right side of Zero and subdivisions on left-hand side of Zero. Take height of scale 5 to 10 mm for getting a look of scale.
After construction of scale mention it’s RF and name of scale as shown.
Show the distance 4 m 6 dm on it as shown.
DIMENSION OF DRAWING
DIMENSION OF OBJECT

## Slide 27
PROBLEM NO.2:- In a map a 36 km distance is shown by a line 45 cms long. Calculate the R.F. and construct
a plain scale to read kilometers and hectometers, for max. 12 km. Show a distance of 8.3 km on it.
CONSTRUCTION:-
a) Calculate R.F.
R.F.= 45 cm/ 36 km = 45/ 36 . 1000 . 100 = 1/ 80,000
Length of scale = R.F. max. distance
= 1/ 80000 12 km
= 15 cm
Draw a line 15 cm long and divide it in 12 equal parts. Each part will represent larger division unit.
Sub divide the first part which will represent second unit or fraction of first unit.
Place ( 0 ) at the end of first unit. Number the units on right side of Zero and subdivisions on left-hand side of Zero. Take height of scale 5 to 10 mm for getting a look of scale.
After construction of scale mention it’s RF and name of scale as shown.
Show the distance 8.3 km on it as shown.
HECTOMETERS
8KM 3HM
0
1
2 3 4 5 6 7 8 9
R.F. = 1/80,000
PLANE SCALE SHOWING KILOMETERS AND HECTOMETERS
10
11
KILOMETERS
10
5
PLAIN SCALE

## Slide 28
PROBLEM NO.3:- The distance between two stations is 210 km. A passenger train covers this distance
in 7 hours. Construct a plain scale to measure time up to a single minute. RF is 1/200,000 Indicate the distance traveled by train in 29 minutes.
CONSTRUCTION:-
a) 210 km in 7 hours. Means speed of the train is 30 km per hour ( 60 minutes)
Length of scale = R.F. max. distance per hour
= 1/ 2,00,000 30km
= 15 cm
15 cm length will represent 30 km and 1 hour i.e. 60 minutes.
Draw a line 15 cm long and divide it in 6 equal parts. Each part will represent 5 km and 10 minutes.
Sub divide the first part in 10 equal parts,which will represent second unit or fraction of first unit. Each smaller part will represent distance traveled in one minute.
Place ( 0 ) at the end of first unit. Number the units on right side of Zero and subdivisions on left-hand side of Zero. Take height of scale 5 to 10 mm for getting a proper look of scale.
Show km on upper side and time in minutes on lower side of the scale as shown.
After construction of scale mention it’s RF and name of scale as shown.
Show the distance traveled in 29 minutes, which is 14.5 km, on it as shown.
PLAIN SCALE
0
40
10
50 MINUTES
MIN
10 20 30
R.F. = 1/100
PLANE SCALE SHOWING METERS AND DECIMETERS.
KM
10
15
20
25 KM
5
DISTANCE TRAVELED IN 29 MINUTES.
14.5 KM
2.5 0 5

## Slide 29: DIAGONAL SCALE
We have seen that the plain scales give only two dimensions, such as a unit and it‟s subunit or it‟s fraction.
X
Y
10
9
8
7
6
5
4
3
2
1
Z
The principle of construction of a diagonal scale is as follows.
Let the XY in figure be a subunit.
From Y draw a perpendicular YZ to a suitable height. Join XZ. Divide YZ in to 10 equal parts.
Draw parallel lines to XY from all these divisions and number them as shown.
From geometry we know that similar triangles have
their like sides proportional.
Consider two similar triangles XYZ and 7’ 7Z,
we have 7Z / YZ = 7’7 / XY (each part being one unit) Means 7’ 7 = 7 / 10. x X Y = 0.7 XY
:.
Similarly
1’ – 1 = 0.1 XY
2’ – 2 = 0.2 XY
Thus, it is very clear that, the sides of small triangles, which are parallel to divided lines, become progressively shorter in length by 0.1 XY.
The solved examples ON NEXT PAGES will make the principles of diagonal scales clear.
The diagonal scales give us three successive dimensions that is a unit, a subunit and a subdivision of a subunit.

## Slide 30
200
R.F. = 1 / 40,00,000
DIAGONAL SCALE SHOWING KILOMETERS.
0
100
300
400
500 KM
50
0
KM 100
KM
PROBLEM NO. 4 : The distance between Delhi and Agra is 200 km.
In a railway map it is represented by a line 5 cm long. Find it’s R.F. Draw a diagonal scale to show single km. And maximum 600 km.
Indicate on it following distances. 1) 222 km 2) 336 km 3) 459 km 4) 569 km
SOLUTION STEPS:
RF = 5 cm / 200 km = 1 / 40, 00, 000
Length of scale = 1 / 40, 00, 000 X 600 X 105 = 15 cm
Draw a line 15 cm long. It will represent 600 km.Divide it in six equal parts.( each will represent 100 km.)
Divide first division in ten equal parts.Each will represent 10 km.Draw a line upward from left end and
mark 10 parts on it of any distance. Name those parts 0 to 10 as shown.Join 9th sub-division of horizontal scale with 10th division of the vertical divisions. Then draw parallel lines to this line from remaining sub divisions and complete diagonal scale.
569 km
459 km
336 km
222 km
10
9
8
7
6
5
4
3
2
1
DIAGONAL SCALE

## Slide 31: DIAGONAL
PROBLEM NO.5: A rectangular plot of land measuring 1.28 hectors is represented on a map by a similar rectangle of 8 sq. cm. Calculate RF of the scale. Draw a diagonal scale to read single meter. Show a distance of 438 m on it.
Draw a line 15 cm long.
It will represent 600 m.Divide it in six equal parts. ( each will represent 100 m.)
Divide first division in ten equal parts.Each will represent 10 m.
Draw a line upward from left end and mark 10 parts on it of any distance.
Name those parts 0 to 10 as shown.Join 9th sub-division
of horizontal scale with 10th division of the vertical divisions. Then draw parallel lines to this line from remaining sub divisions and complete diagonal scale.
SCALE
SOLUTION :
1 hector = 10, 000 sq. meters
1.28 hectors = 1.28 X 10, 000 sq. meters
= 1.28 X 104 X 104 sq. cm
8 sq. cm area on map represents
= 1.28 X 104 X 104 sq. cm on land 1 cm sq. on map represents
= 1.28 X 10 4 X 104 / 8 sq cm on land 1 cm on map represent
= 1.28 X 10 4 X 104 / 8 cm
= 4, 000 cm
1 cm on drawing represent 4, 000 cm, Means RF = 1 / 4000 Assuming length of scale 15 cm, it will represent 600 m.
0
100
300
400
50
10
9
8
7
6
5
4
3
2
1
0
500 M
M
M 100
438 meters
200
R.F. = 1 / 4000
DIAGONAL SCALE SHOWING METERS.

## Slide 32
10
9
8
7
6
5
4
3
2
1
0
15 CENTIMETRES
MM
CM
5 4
3
2 1 0 5 10
R.F. = 1 / 2.5
DIAGONAL SCALE SHOWING CENTIMETERS.
PROBLEM NO.6:. Draw a diagonal scale of R.F. 1: 2.5, showing centimeters and millimeters and long enough to measure up to 20 centimeters.
SOLUTION STEPS:
R.F. = 1 / 2.5
Length of scale = 1 / 2.5 X 20 cm.
= 8 cm.
Draw a line 8 cm long and divide it in to 4 equal parts. (Each part will represent a length of 5 cm.)
Divide the first part into 5 equal divisions. (Each will show 1 cm.)
At the left hand end of the line, draw a vertical line and on it step-off 10 equal divisions of any length.
Complete the scale as explained in previous problems.
Show the distance 13.4 cm on it.
13 .4 CM
DIAGONAL SCALE

## Slide 33
Planes.
Pattern of planes & Pattern of views
ORTHOGRAPHIC PROJECTIONS:
IT IS A TECHNICAL DRAWING IN WHICH DIFFERENT VIEWS OF AN OBJECT
ARE PROJECTED ON DIFFERENT REFERENCE PLANES OBSERVING PERPENDICULAR TO RESPECTIVE REFERENCE PLANE
Different Reference planes are
Horizontal Plane (HP), Vertical Frontal Plane ( VP )
Side Or Profile Plane ( PP)
And
Different Views are Front View (FV), Top View (TV) and Side View (SV)
FV is a view projected on VP. TV is a view projected on HP. SV is a view projected on PP.
IMPORTANT TERMS OF ORTHOGRAPHIC PROJECTIONS:
1
2
3 Methods of drawing Orthographic Projections

## Slide 34: PLANES


A.V.P.
 to Hp &  to Vp
PRINCIPAL PLANES
HP AND VP
AUXILIARY PLANES
Auxiliary Vertical Plane (A.V.P.)
Profile Plane ( P.P.)
Auxiliary Inclined Plane
(A.I.P.)
1

## Slide 35
THIS IS A PICTORIAL SET-UP OF ALL THREE PLANES.
ARROW DIRECTION IS A NORMAL WAY OF OBSERVING THE OBJECT. BUT IN THIS DIRECTION ONLY VP AND A VIEW ON IT (FV) CAN BE SEEN. THE OTHER PLANES AND VIEWS ON THOSE CAN NOT BE SEEN.
PROCEDURE TO SOLVE ABOVE PROBLEM:-
HP IS ROTATED DOWNWARD 900 AND
BROUGHT IN THE PLANE OF VP.
PP IS ROTATED IN RIGHT SIDE 900
AND
BROUGHT IN THE PLANE OF VP.
X
Y
X
Y
VP
HP
PP
FV
ACTUAL PATTERN OF PLANES & VIEWS OF ORTHOGRAPHIC PROJECTIONS DRAWN IN
FIRST ANGLE METHOD OF PROJECTIONS
LSV
TV
TO MAKE THOSE PLANES ALSO VISIBLE FROM THE ARROW DIRECTION,
HP IS ROTATED 900 DOUNWARD
PP, 900 IN RIGHT SIDE DIRECTION.
THIS WAY BOTH PLANES ARE BROUGHT IN THE SAME PLANE CONTAINING VP.
PATTERN OF PLANES & VIEWS (First Angle Method)
2
Click to view Animation
On clicking the button if a warning comes please click YES to continue, this program is safe for your pc.

## Slide 36: Methods of Drawing Orthographic Projections
First Angle Projections Method
Here views are drawn by placing object
in 1st Quadrant
( Fv above X-y, Tv below X-y )
Third Angle Projections Method
Here views are drawn by placing object
in 3rd Quadrant.
( Tv above X-y, Fv below X-y )
FV
TV
X
Y
X
Y
G
L
TV
FV
SYMBOLIC
PRESENTATION OF BOTH METHODS WITH AN OBJECT
STANDING ON HP ( GROUND) ON IT’S BASE.
NOTE:-
HP term is used in 1st Angle method &
For the same
Ground term is used
in 3rd Angle method of projections
3

## Slide 37: FIRST ANGLE PROJECTION
FOR T.V.
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE SITUATED IN FIRST QUADRANT MEANS
ABOVE HP & INFRONT OF VP.
OBJECT IS INBETWEEN OBSERVER & PLANE.
ACTUAL PATTERN OF PLANES & VIEWS
IN
FIRST ANGLE METHOD OF PROJECTIONS
X
Y
VP
HP
PP
FV
LSV
TV

## Slide 38: THIRD ANGLE PROJECTION
FOR T.V.
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE SITUATED IN THIRD QUADRANT ( BELOW HP & BEHIND OF VP. )
PLANES BEING TRANSPERENT
AND INBETWEEN OBSERVER & OBJECT.
ACTUAL PATTERN OF PLANES & VIEWS
OF
THIRD ANGLE PROJECTIONS
X
Y
TV
LSV
FV

## Slide 39: ORTHOGRAPHIC PROJECTIONS
OF POINTS, LINES, PLANES, AND SOLIDS.
TO DRAW PROJECTIONS OF ANY OBJECT, ONE MUST HAVE FOLLOWING INFORMATION
OBJECT
{ WITH IT‟S DESCRIPTION, WELL DEFINED.}
OBSERVER
{ ALWAYS OBSERVING PERPENDICULAR TO RESP. REF.PLANE}.
LOCATION OF OBJECT,
{ MEANS IT‟S POSITION WITH REFFERENCE TO H.P. & V.P.}
TERMS „ABOVE‟ & „BELOW‟ WITH RESPECTIVE TO H.P. AND TERMS „INFRONT‟ & „BEHIND‟ WITH RESPECTIVE TO V.P
FORM 4 QUADRANTS.
OBJECTS CAN BE PLACED IN ANY ONE OF THESE 4 QUADRANTS.
IT IS INTERESTING TO LEARN THE EFFECT ON THE POSITIONS OF VIEWS ( FV, TV ) OF THE OBJECT WITH RESP. TO X-Y LINE, WHEN PLACED IN DIFFERENT QUADRANTS.
STUDY ILLUSTRATIONS GIVEN ON HEXT PAGES AND NOTE THE RESULTS.TO MAKE IT EASY HERE A POINT A IS TAKEN AS AN OBJECT. BECAUSE IT’S ALL VIEWS ARE JUST POINTS.

## Slide 40: NOTATIONS
FOLLOWING NOTATIONS SHOULD BE FOLLOWED WHILE NAMEING DIFFERENT VIEWS IN ORTHOGRAPHIC PROJECTIONS.
SAME SYSTEM OF NOTATIONS SHOULD BE FOLLOWED
INCASE NUMBERS, LIKE 1, 2, 3 – ARE USED.
OBJECT | POINT | A | LINE AB
IT‟S TOP VIEW IT‟S FRONT VIEW IT‟S SIDE VIEW | a a‟ a” | a b a‟ b‟ a” b” | 

## Slide 41
X
Y
1ST Quad.
2nd
Quad.
3rd
Quad.
4th Quad.
X Y
VP
HP
Observer
THIS QUADRANT PATTERN,
IF OBSERVED ALONG X-Y LINE ( IN RED ARROW DIRECTION) WILL EXACTLY APPEAR AS SHOWN ON RIGHT SIDE AND HENCE,
IT IS FURTHER USED TO UNDERSTAND ILLUSTRATION PROPERLLY.

## Slide 42
HP
VP
a’
a
A
POINT A IN 1ST QUADRANT
OBSERVER
VP
HP
OBSERVER
a’
a
POINT A IN 2ND QUADRANT
A
OBSERVER
a
a’
3RD
QUADRANT
HP
VP
A
POINT A IN
OBSERVER
a
a’
POINT A IN
4TH
QUADRANT
HP
VP
A
Point A is Placed In different quadrants
and it‟s Fv & Tv are brought in same plane for Observer to see clearly.
Fv is visible as it is a view on VP. But as Tv is is a view on Hp, it is rotated downward 900, In clockwise direction.The
In front part of
Hp comes below
xy line and the part behind Vp comes above.
Observe and note the process.

## Slide 43: PROJECTIONS OF A POINT IN FIRST QUADRANT.
A
a
a’
a
a’ A
a
A
a’
X
Y
X
Y
X
Y
For Tv
For Tv
For Tv
POINT A ABOVE HP & INFRONT OF VP
POINT A IN HP & INFRONT OF VP
POINT A ABOVE HP & IN VP
PICTORIAL PRESENTATION
PICTORIAL PRESENTATION
ORTHOGRAPHIC PRESENTATIONS OF ALL ABOVE CASES.
X
Y
a
a’
VP
HP
X
Y
a’
VP
HP
a
X
Y
a
VP
HP
a’
Fv above xy, Tv below xy.
Fv above xy, Tv on xy.
Fv on xy, Tv below xy.

## Slide 44: PROJECTIONS OF STRAIGHT LINES.
SIMPLE CASES OF THE LINE
A VERTICAL LINE ( LINE PERPENDICULAR TO HP & // TO VP)
LINE PARALLEL TO BOTH HP & VP.
LINE INCLINED TO HP & PARALLEL TO VP.
LINE INCLINED TO VP & PARALLEL TO HP.
LINE INCLINED TO BOTH HP & VP.
STUDY ILLUSTRATIONS GIVEN ON NEXT PAGE SHOWING CLEARLY THE NATURE OF FV & TV OF LINES LISTED ABOVE AND NOTE RESULTS.
INFORMATION REGARDING A LINE means
IT‟S LENGTH,
POSITION OF IT‟S ENDS WITH HP & VP
IT‟S INCLINATIONS WITH HP & VP WILL BE GIVEN. AIM:- TO DRAW IT‟S PROJECTIONS - MEANS FV & TV.

## Slide 45
X
Y
X
Y
b’
a’
b
a
a b
b’
B
A
TV
FV
A
B
X
Y
V.P.
a’
b’
Fv
Tv a b
X
Y
H.P.
V.P.
a
b
a’
b’
Fv
Tv
For Tv
For Tv
Note:
Fv is a vertical line Showing True Length &
Tv is a point.
Note:
Fv & Tv both are
// to xy &
both show T. L.
1.
(Pictorial Presentation)
2.
A Line perpendicular to Hp
&
// to Vp
A Line
// to Hp &
// to Vp
Orthographic Pattern
H.P.
Orthographic Pattern
(Pictorial Presentation)
a’

## Slide 46
Y
A
B
b’
a’
b
a


Ø
a
b
a’
b’
B
A
Ø
X
Y
V.P.
T.V.
a
b
a’
b’

X
Y
V.P.
Ø
a
b
H.P.
a’
b’
Tv
Fv
Tv inclined to xy Fv parallel to xy.
3.
A Line inclined to Hp and
parallel to Vp
(Pictorial presentation)
X
4.
A Line inclined to Vp
and
parallel to Hp
(Pictorial presentation)
Fv inclined to xy Tv parallel to xy.
H.P.
Orthographic Projections

## Slide 47
X
Y
a’
b’
a
b
B
A


For Tv
T.V.
X
Y
a’
b’
a
b


T.V.
For Tv
B
A
X
Y

H.P.
a
b
FV

TV
a’
V.P.
b’
A Line inclined to both
Hp and Vp
(Pictorial presentation)
5.
Note These Facts:-
Both Fv & Tv are inclined to xy.
(No view is parallel to xy)
Both Fv & Tv are reduced lengths. (No view shows True Length)
Orthographic Projections
Fv is seen on Vp clearly.
To see Tv clearly, HP is rotated 900 downwards, Hence it comes below xy.
On removal of object
i.e. Line AB
Fv as a image on Vp. Tv as a image on Hp,

## Slide 48
X
Y
H.P.
V.P.
X
Y

H.P.
V.P.
a
b
TV
a’
b’
FV
TV
b2
1
b ’
TL
X
Y

H.P.
V.P.
a
b
TV
FV
a’ 
b’
Here TV (ab) is not // to XY line Hence it’s corresponding FV a’ b’ is not showing
True Length & True Inclination with Hp.
In this sketch, TV is rotated
and made // to XY line. Hence it’s corresponding FV a’ b1’ Is showing
True Length &
True Inclination with Hp.
Note the procedure When Fv & Tv known, How to find True Length.
(Views are rotated to determine True Length & it‟s inclinations with Hp & Vp).
Note the procedure When True Length is known,
How to locate Fv & Tv. (Component a-1 of TL is drawn which is further rotated
to determine Fv)
1
a
a’
b’
1’
b

b1’


b1
Ø
Orthographic Projections Means Fv & Tv of Line AB are shown below,
with their apparent Inclinations
 & 
Here a -1 is component of TL ab1 gives length of Fv. Hence it is brought Up to
Locus of a’ and further rotated to get point b’. a’ b’ will be Fv.
Similarly drawing component
of other TL(a‟ b1„) Tv can be drawn.


## Slide 49
Views are always rotated, made horizontal & further extended to locate TL,  & Ø
Also Remember
True Length is never rotated. It‟s horizontal component is drawn & it is further rotated to locate view.
X
Y
H.P.
The most important diagram showing graphical relations among all important parameters of this topic.
Study and memorize it as a CIRCUIT DIAGRAM
And use in solving various problems.
V.P.
1
a
b

b
1
Ø
LFV
a’
b’
1’
1
b ’


LTV
Distance between End Projectors.
b’ & b1’ on same locus. b & b1 on same locus.
NOTE this
 &  Construct with a’
Ø &  Construct with a
1) True Length ( TL) – a’ b1’ & a b |  |  |  |  |  | 
Angle of TL with Hp -  Important Angle of TL with Vp – Ø TEN parameters to be remembered Angle of FV with xy –  with Notations Angle of TV with xy –  used here onward LTV (length of FV) – Component (a-1) LFV (length of TV) – Component (a‟-1‟) Position of A- Distances of a & a‟ from xy Position of B- Distances of b & b‟ from xy Distance between End Projectors |  |  |  |  |  | 

## Slide 50
a’
b’
a
X
Y
b’1
b b1
Ø

GROUP (A)
GENERAL CASES OF THE LINE INCLINED TO BOTH HP & VP
( based on 10 parameters).
PROBLEM 1)
Line AB is 75 mm long and it is 300 & 400 Inclined to Hp & Vp respectively. End A is 12mm above Hp and 10 mm in front of Vp.
Draw projections. Line is in 1st quadrant.
SOLUTION STEPS:
Draw xy line and one projector.
Locate a‟ 12mm above xy line & a 10mm below xy line.
Take 300 angle from a‟ & 400 from a and mark TL I.e. 75mm on both lines. Name those points b1‟ and b1 respectively.
Join both points with a‟ and a resp.
Draw horizontal lines (Locus) from both points.
Draw horizontal component of TL a b1 from point b1 and name it 1.
( the length a-1 gives length of Fv as we have seen already.)
Extend it up to locus of a‟ and rotating a‟ as center locate b‟ as shown. Join a‟ b‟ as Fv.
From b‟ drop a projector down ward & get point b. Join a & b
I.e. Tv.
1
LFV
TL
TL
FV
TV

## Slide 51: PROBLEM 2:
X
y
a
a’
b1
LFV 1
b’1
550
b
Line AB 75mm long makes 450 inclination with Vp while it’s Fv makes 550. End A is 10 mm above Hp and 15 mm in front of Vp.If line is in 1st quadrant draw it’s projections and find it’s inclination with Hp.
b’
LOCUS OF b
LOCUS OF
Solution Steps:-
Draw x-y line.
Draw one projector for a‟ & a 3.Locate a’ 10mm above x-y & Tv a 15 mm below xy.
Draw a line 450 inclined to xy from point a and cut TL 75 mm on it and name that point b1 Draw locus from point b1
Take 550 angle from a’ for Fv above xy line.
Draw a vertical line from b1
up to locus of a and name it 1. It is horizontal component of TL & is LFV.
Continue it to locus of a’ and rotate upward up to the line of Fv and name it b’.This a’ b’ line is Fv.
Drop a projector from b‟ on locus from point b1 and name intersecting point b. Line a b is Tv of line AB.
Draw locus from b’ and from
a’ with TL distance cut point b1‘
Join a’ b1’ as TL and measure it‟s angle at a’.
It will be true angle of line with HP.

## Slide 52: PROBLEM 3:
X
a’
y
a
b’
500
b
600
b1
b’1


Fv of line AB is 500 inclined to xy and measures 55 mm long while it’s Tv is 600 inclined to xy line. If end A is 10 mm above Hp and 15 mm in front of Vp, draw it’s projections,find TL, inclinations of line
with Hp & Vp.
SOLUTION STEPS:
1.Draw xy line and one projector. 2.Locate a’ 10 mm above xy and a 15 mm below xy line.
3.Draw locus from these points. 4.Draw Fv 500 to xy from a’ and mark b’ Cutting 55mm on it.
Similarly draw Tv 600 to xy
from a & drawing projector from b’ Locate point b and join a b.
Then rotating views as shown, locate True Lengths ab1 & a’b1’ and their angles with Hp and Vp.

## Slide 53
X
Y
a’
1’
a
b’1
LTV
b1
1
b
LFV


PROBLEM 4 :-
Line AB is 75 mm long .It‟s Fv and Tv measure 50 mm & 60 mm long respectively. End A is 10 mm above Hp and 15 mm in front of Vp. Draw projections of line AB if end B is in first quadrant.Find angle with Hp and Vp.
b’
SOLUTION STEPS:
1.Draw xy line and one projector. 2.Locate a’ 10 mm above xy and a 15 mm below xy line.
3.Draw locus from these points. 4.Cut 60mm distance on locus of a’
& mark 1’ on it as it is LTV.
Similarly Similarly cut 50mm on
locus of a and mark point 1 as it is LFV.
From 1’ draw a vertical line upward and from a’ taking TL ( 75mm ) in compass, mark b’1 point on it.
Join a’ b’1 points.
Draw locus from b’1
With same steps below get b1 point and draw also locus from it.
Now rotating one of the components
I.e. a-1 locate b’ and join a’ with it to get Fv.
10. Locate tv similarly and measure
Angles 

&

## Slide 54: PROJECTIONS OF PLANES
In this topic various plane figures are the objects.
What is usually asked in the problem?
To draw their projections means F.V, T.V. & S.V.
What will be given in the problem?
Description of the plane figure.
It’s position with HP and VP.
In which manner it’s position with HP & VP will be described?
Inclination of it’s SURFACE with one of the reference planes will be given.
Inclination of one of it’s EDGES with other reference plane will be given
(Hence this will be a case of an object inclined to both reference Planes.)
Study the illustration showing
surface & side inclination given on next page.

## Slide 55
HP
VP
VP
VP
a’
d’
c’
b’
HP
a
b
d
c
a1’
d1’ c1’
b1’
HP
a1
b1
c1
d1
CASE OF A RECTANGLE – OBSERVE AND NOTE ALL STEPS.
SURFACE PARALLEL TO HP
PICTORIAL PRESENTATION
SURFACE INCLINED TO HP
PICTORIAL PRESENTATION
ONE SMALL SIDE INCLINED TO VP
PICTORIAL PRESENTATION
ORTHOGRAPHIC
TV-True Shape FV- Line // to xy
ORTHOGRAPHIC
FV- Inclined to XY TV- Reduced Shape
ORTHOGRAPHIC
FV- Apparent Shape TV-Previous Shape
A
B
C

## Slide 56
PROCEDURE OF SOLVING THE PROBLEM:
IN THREE STEPS EACH PROBLEM CAN BE SOLVED:( As Shown In Previous Illustration )
STEP 1. Assume suitable conditions & draw Fv & Tv of initial position. STEP 2. Now consider surface inclination & draw 2nd Fv & Tv.
STEP 3. After this,consider side/edge inclination and draw 3rd ( final) Fv & Tv.
ASSUMPTIONS FOR INITIAL POSITION:
(Initial Position means assuming surface // to HP or VP)
If in problem surface is inclined to HP – assume it // HP Or If surface is inclined to VP – assume it // to VP
Now if surface is assumed // to HP- It’s TV will show True Shape. And If surface is assumed // to VP – It’s FV will show True Shape.
Hence begin with drawing TV or FV as True Shape.
While drawing this True Shape –
keep one side/edge ( which is making inclination) perpendicular to xy line
( similar to pair no. on previous page illustration ).
A
B
Now Complete STEP 2. By making surface inclined to the resp plane & project it‟s other view.
(Ref. 2nd pair on previous page illustration )
C
Now Complete STEP 3. By making side inclined to the resp plane & project it‟s other view.
(Ref. 3nd pair on previous page illustration )
APPLY SAME STEPS TO SOLVE NEXT ELEVEN PROBLEMS

## Slide 57
X
Y
a
b
c
d
c’d’
a1
b1
c1
d1
a’b’
c’1 d’1
b’1
a’1
a’b’450
300
Problem 1:
Rectangle 30mm and 50mm sides is resting on HP on one small side which is 300 inclined to VP,while the surface of the plane makes 450 inclination with HP. Draw it’s projections.
Read problem and answer following questions
Surface inclined to which plane? ------- HP
Assumption for initial position? ------// to HP
So which view will show True shape? --- TV
Which side will be vertical? ---One small side.
Hence begin with TV, draw rectangle below X-Y drawing one small side vertical.
Surface // to Hp
Surface inclined to Hp
d’c’
Side Inclined to Vp

## Slide 58
Problem 2:
A 300 – 600 set square of longest side 100 mm long, is in VP and 300 inclined to HP while it’s surface is 450 inclined to VP.Draw it’s projections
(Surface & Side inclinations directly given)
Read problem and answer following questions 1 .Surface inclined to which plane? ------- VP
Assumption for initial position? ------// to VP
So which view will show True shape? --- FV
Which side will be vertical? ------longest side.
c1
X
Y
300
450
a’1
b’1
c’
1
a
c
a’
b1
b’
a b
a1
b
c
a’1
b’1
c’
side inclined to Hp
c’1
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
Surface // to Vp
Surface inclined to Vp

## Slide 59
c
c1
X
Y
450
a’1
b’1
c’1
a
c
a’
b1
b’
a
b
a1
b
b’1
c’1
a’1
c’
35
10
Problem 3:
A 300 – 600 set square of longest side 100 mm long is in VP and it’s surface
450 inclined to VP. One end of longest side is 10 mm and other end is 35 mm above HP. Draw it’s projections
(Surface inclination directly given. Side inclination indirectly given)
Read problem and answer following questions 1 .Surface inclined to which plane? ------- VP
Assumption for initial position? ------// to VP
So which view will show True shape? --- FV
Which side will be vertical? ------longest side.
Hence begin with FV, draw triangle above X-Y keeping longest side vertical.
First TWO steps are similar to previous problem. Note the manner in which side inclination is given. End A 35 mm above Hp & End B is 10 mm above Hp.
So redraw 2nd Fv as final Fv placing these ends as said.

## Slide 60: Problem 4:
b’ a’
d’
b1
d
c1
a
c’e’
b
c
d1
1
a1
e’1
c’1
b1
c1
d1
Read problem and answer following questions
Surface inclined to which plane? ------- HP
Assumption for initial position? ------ // to HP
So which view will show True shape? --- TV
Which side will be vertical? -------- any side. Hence begin with TV,draw pentagon below X-Y line, taking one side vertical.
d’ d’1
b’ a’
c’e’
e1
e1
a’1
X
b’ Y
45
0
a1 300
e
A regular pentagon of 30 mm sides is
resting on HP on one of it’s sides with it’s
surface 450 inclined to HP.
Draw it’s projections when the side in HP makes 300 angle with VP
SURFACE AND SIDE INCLINATIONS ARE DIRECTLY GIVEN.

## Slide 61
Problem 5:
A regular pentagon of 30 mm sides is resting on HP on one of it’s sides while it’s opposite vertex (corner) is 30 mm above HP.
Draw projections when side in HP is 300 inclined to VP.
Read problem and answer following questions
Surface inclined to which plane? ------- HP
Assumption for initial position? ------ // to HP
So which view will show True shape? --- TV
Which side will be vertical? --------any side. Hence begin with TV,draw pentagon below X-Y line, taking one side vertical.
d’
a’
b’
c’e’
a
1
b1
c1
d1
e1
b1
c1
d1
a1
e1
b’1
e’
1
c’1
d’1
a’1
X
Y
b’ a’
d’
c’e’
30
a
b
c
d
e
30
0
SURFACE INCLINATION INDIRECTLY GIVEN SIDE INCLINATION DIRECTLY GIVEN:
ONLY CHANGE is
the manner in which surface inclination is described: One side on Hp & it’s opposite corner 30 mm above Hp.
Hence redraw 1st Fv as a 2nd Fv making above arrangement.
Keep a’b’ on xy & d’ 30 mm above xy.

## Slide 62
a
d
a’
b’ d’
c’
X
Y
ca1
b b1
d1
c1
450
300
a’
1
b’
1
c’1
d’
1
a1
b1
d1
c
1
a
d
c
b
a’
b’ d’
c’
300
b’1
a’1
c’1
d’1
Problem 8: A circle of 50 mm diameter is resting on Hp on end A of it’s diameter AC which is 300 inclined to Hp while it’s Tv
is 450 inclined to Vp.Draw it’s projections.
Problem 9: A circle of 50 mm diameter is resting on Hp on end A of it’s diameter AC which is 300 inclined to Hp while it makes 450 inclined to Vp. Draw it’s projections.
Read problem and answer following questions
Surface inclined to which plane? ------- HP
Assumption for initial position? ------ // to HP
So which view will show True shape? --- TV
Which diameter horizontal? ---------- AC Hence begin with TV,draw rhombus below X-Y line, taking longer diagonal // to X-Y
The difference in these two problems is in step 3 only.
In problem no.8 inclination of Tv of that AC is given,It could be drawn directly as shown in 3rd step.
While in no.9 angle of AC itself i.e. it’s TL, is given. Hence here angle of TL is taken,locus of c1 Is drawn and then LTV I.e. a1 c1 is marked and
final TV was completed.Study illustration carefully.
Note the difference in construction of 3rd step in both solutions.

## Slide 63
Problem 10: End A of diameter AB of a circle is in HP A nd end B is in VP.Diameter AB, 50 mm long is 300 & 600 inclined to HP & VP respectively.
Draw projections of circle.
The problem is similar to previous problem of circle – no.9. But in the 3rd step there is one more change.
Like 9th problem True Length inclination of dia.AB is definitely expected
but if you carefully note - the the SUM of it‟s inclinations with HP & VP is 900. Means Line AB lies in a Profile Plane.
Hence it‟s both Tv & Fv must arrive on one single projector.
So do the construction accordingly AND note the case carefully..
SOLVE SEPARATELY ON DRAWING SHEET
GIVING NAMES TO VARIOUS
POINTS AS USUAL,
AS THE CASE IS IMPORTANT
X
Y
300
600
Read problem and answer following questions
Surface inclined to which plane? ------- HP
Assumption for initial position? ------ // to HP
So which view will show True shape? --- TV
Which diameter horizontal? ---------- AB Hence begin with TV,draw CIRCLE below X-Y line, taking DIA. AB // to X-Y

## Slide 64: Read problem and answer following questions
As 3rd step redraw 2nd Tv keeping
side DE on xy line. Because it is in VP as said in problem.
X
Y
a
b
c
d
e
f
Problem 11:
A hexagonal lamina has its one side in HP and Its apposite parallel side is 25mm above Hp and In Vp. Draw it’s projections.
Take side of hexagon 30 mm long.
ONLY CHANGE is the manner in which surface inclination
is described:
One side on Hp & it’s opposite side 25 mm above Hp. Hence redraw 1st Fv as a 2nd Fv making above arrangement. Keep a’b’ on xy & d’e’ 25 mm above xy.
25
d’e’
c’ f’
a’b’
a
1
b1
c1
d1
e
1
f1
1
c ’
a’ b’
1
f’1
d’1
e’1
f1
a1
c1
b1
1
e1 d1
Surface inclined to which plane? ------- HP
Assumption for initial position? ------ // to HP
So which view will show True shape? --- TV
Which diameter horizontal? ---------- AC Hence begin with TV,draw rhombus below X-Y line, taking longer diagonal // to X-Y

## Slide 65: FREELY SUSPENDED CASES.
A
B
C
H
H/3
G
X
Y
a’
b’
c’
g‟
b
a,g
c
450
a’1
c’1
b’1
g’
1
In this case the plane of the figure always remains perpendicular to Hp.
It may remain parallel or inclined to Vp.
Hence TV in this case will be always a LINE view.
Assuming surface // to Vp, draw true shape in suspended position as FV. (Here keep line joining point of contact & centroid of fig. vertical ) 5.Always begin with FV as a True Shape but in a suspended position.
AS shown in 1st FV.
IMPORTANT POINTS
Problem 12:
An isosceles triangle of 40 mm long base side, 60 mm long altitude Is freely suspended from one corner of Base side.It‟s plane is 450 inclined to Vp. Draw it‟s projections.
Similarly solve next problem of Semi-circle
First draw a given triangle With given dimensions, Locate it‟s centroid position And
join it with point of suspension.

## Slide 66: IMPORTANT POINTS
A
P
20 mm
G
CG
X
Y
e’
c’
d’
b’
a’
p’
g’
b c a p,g d
e
Problem 13
:A semicircle of 100 mm diameter is suspended from a point on its
straight edge 30 mm from the midpoint of that edge so that the surface makes an angle of 450 with VP.
Draw its projections.
First draw a given semicircle With given diameter,
Locate it‟s centroid position And
join it with point of suspension.
In this case the plane of the figure always remains perpendicular to Hp.
It may remain parallel or inclined to Vp.
Hence TV in this case will be always a LINE view.
Assuming surface // to Vp, draw true shape in suspended position as FV. (Here keep line joining point of contact & centroid of fig. vertical ) 5.Always begin with FV as a True Shape but in a suspended position.
AS shown in 1st FV.

## Slide 67: SOLIDS
Cylinder
Prisms
Triangular Square Pentagonal
Hexagonal
Hexagonal
Cone
Pyramids
Cube
( A solid having
six square faces)
Triangular Square Pentagonal
Tetrahedron
( A solid having Four triangular faces)
To understand and remember various solids in this subject properly, those are classified & arranged in to two major groups.
Group A Group B
Solids having top and base of same shape Solids having base of some shape
and just a point as a top, called apex.

## Slide 68: SOLIDS Dimensional parameters of different solids.
Top
Rectangular Face Longer Edge
Base
Edge of Base
Corner of base
Corner of base
Triangular Face
Slant Edge
Base
Apex
Square Prism Square Pyramid
Cylinder
Cone
Edge of Base
Base
Apex
Base
Generators
Imaginary lines generating curved surface of cylinder & cone.
Sections of solids( top & base not parallel)
Frustum of cone & pyramids.
( top & base parallel to each other)

## Slide 69
Y
RESTING ON H.P
On one point of base circle.
(Axis inclined to Hp And // to Vp)
LYING ON H.P
On one generator.
(Axis inclined to Hp And // to Vp)
X
While observing Fv, x-y line represents Horizontal Plane. (Hp)
STANDING ON H.P
On it’s base.
(Axis perpendicular to Hp And // to Vp.)
F.V. F.V.
STANDING ON V.P
On it’s base.
Axis perpendicular to Vp And // to Hp
RESTING ON V.P
On one point of base circle.
Axis inclined to Vp And // to Hp
LYING ON V.P
On one generator.
Axis inclined to Vp And // to Hp
X
Y
F.V.
T.V.
T.V.
T.V.
While observing Tv, x-y line represents Vertical Plane. (Vp)

## Slide 70: STEPS TO SOLVE PROBLEMS IN SOLIDS
Problem is solved in three steps:
STEP 1: ASSUME SOLID STANDING ON THE PLANE WITH WHICH IT IS MAKING INCLINATION. ( IF IT IS INCLINED TO HP, ASSUME IT STANDING ON HP)
( IF IT IS INCLINED TO VP, ASSUME IT STANDING ON VP)
IF STANDING ON HP - IT’S TV WILL BE TRUE SHAPE OF IT’S BASE OR TOP: IF STANDING ON VP - IT’S FV WILL BE TRUE SHAPE OF IT’S BASE OR TOP. BEGIN WITH THIS VIEW:
IT’S OTHER VIEW WILL BE A RECTANGLE ( IF SOLID IS CYLINDER OR ONE OF THE PRISMS): IT’S OTHER VIEW WILL BE A TRIANGLE ( IF SOLID IS CONE OR ONE OF THE PYRAMIDS):
DRAW FV & TV OF THAT SOLID IN STANDING POSITION:
STEP 2: CONSIDERING SOLID’S INCLINATION ( AXIS POSITION ) DRAW IT’S FV & TV.
STEP 3: IN LAST STEP, CONSIDERING REMAINING INCLINATION, DRAW IT’S FINAL FV & TV.
AXIS AXIS VERTICAL INCLINED HP
AXIS INCLINED VP
AXIS
INCLINED VP
AXIS TO VP
er
AXIS INCLINED VP
INCLINED HP
er
AXIS
AXIS TO VP INCLINED
VP
INCLINED HP
GENERAL PATTERN ( THREE STEPS ) OF SOLUTION:
GROUP B SOLID. CONE
GROUP A SOLID. CYLINDER
AXIS AXIS VERTICAL INCLINED HP
GROUP B SOLID. CONE
AXIS
GROUP A SOLID.
CYLINDER
AXIS
Three steps
If solid is inclined to Hp
Three steps
If solid is inclined to Hp
Three steps
If solid is inclined to Vp
Study Next Twelve Problems and Practice them separately !!
Three steps
If solid is inclined to Vp

## Slide 71: CATEGORIES OF ILLUSTRATED PROBLEMS!
PROBLEM NO.1, 2, 3, 4 GENERAL CASES OF SOLIDS INCLINED TO HP & VP
PROBLEM NO. 5 & 6 CASES OF CUBE & TETRAHEDRON
PROBLEM NO. 7 | CASE | OF FREELY SUSPENDED SOLID WITH SIDE VIEW.
PROBLEM NO. 8 | CASE | OF CUBE ( WITH SIDE VIEW)
PROBLEM NO. 9 | CASE | OF TRUE LENGTH INCLINATION WITH HP & VP.
PROBLEM NO. 10 & 11 | CASES | OF COMPOSITE SOLIDS. (AUXILIARY PLANE)
PROBLEM NO. 12 | CASE | OF A FRUSTUM (AUXILIARY PLANE)

## Slide 72
X
Y
a
b
c
d
o
o’
c’d’
a’b’
o1
d1
b1
c1
a1
a’1
d’1
c’1
b’1
o’1
a1
(APEX
NEARER TO V.P).
(APEX AWAY
FROM V.P.)
Problem 1.
A square pyramid, 40
mm base sides and axis 60 mm long, has a triangular face on the ground and the vertical plane containing the axis makes an angle of 450 with the VP. Draw its projections. Take apex nearer to VP
Solution Steps :
Triangular face on Hp , means it is lying on Hp:
Assume it standing on Hp.
It’s Tv will show True Shape of base( square)
Draw square of 40mm sides with one side vertical Tv & taking 50 mm axis project Fv. ( a triangle)
Name all points as shown in illustration.
Draw 2nd Fv in lying position I.e.o’c’d’ face on xy. And project it’s Tv. 6.Make visible lines dark and hidden dotted, as per the procedure.
7.Then construct remaining inclination with Vp
( Vp containing axis ic the center line of 2nd Tv.Make it 450 to xy as shown take apex near to xy, as it is nearer to Vp) & project final Fv.
For dark and dotted lines
1.Draw proper outline of new view DARK. 2. Decide direction of an observer.
Select nearest point to observer and draw all lines starting from it-dark.
Select farthest point to observer and draw all lines (remaining)from it- dotted.

## Slide 73
Problem 2:
A cone 40 mm diameter and 50 mm axis
is resting on one generator on Hp which makes 300 inclination with Vp Draw it’s projections.
h
a
b
c
d
g
f
X
Y
’
f’ d’ e’
a’ h’b’ c’ g
o’
o’
a1
h1
g1
f1
e e1
d1
c
1
b1
a1
c1
b1
d
1
e1
f1
g1
h
1
o1
a’1
b’1
c’
1
d’
1
e’1
f’1
g’1
h’
1
o
1
o1
30
Solution Steps:
Resting on Hp on one generator, means lying on Hp: 1.Assume it standing on Hp.
It’s Tv will show True Shape of base( circle )
Draw 40mm dia. Circle as Tv &
taking 50 mm axis project Fv. ( a triangle) 4.Name all points as shown in illustration.
Draw 2nd Fv in lying position I.e.o’e’ on xy. And project it’s Tv below xy.
Make visible lines dark and hidden dotted, as per the procedure.
Then construct remaining inclination with Vp
( generator o1e1 300 to xy as shown) & project final Fv.
For dark and dotted lines
Draw proper outline of new vie DARK.
Decide direction of an observer.
Select nearest point to observer and draw all lines starting from it-dark.
Select farthest point to observer and draw all lines (remaining) from it- dotted.

## Slide 74
X
Y
a
c
1
2 4
3
1’a’
2’ b’
b d
3’
4’d’
450
4’
3’
2’
1’
d’
c’
b’
c’ a’
350
a1
b
1
c1
d1
1
2
3
4
Problem 3:
A cylinder 40 mm diameter and 50 mm
axis is resting on one point of a base
circle on Vp while it’s axis makes 450
Draw projections..
Solution Steps:
Resting on Vp on one point of base, means inclined to Vp: 1.Assume it standing on Vp
It’s Fv will show True Shape of base & top( circle )
Draw 40mm dia. Circle as Fv & taking 50 mm axis project Tv. ( a Rectangle)
with Vp and Fv of the axis 350 with Hp. 4.Name all points as shown in illustration.
5.Draw 2nd Tv making axis 450 to xy And project it’s Fv above xy. 6.Make visible lines dark and hidden dotted, as per the procedure. 7.Then construct remaining inclination with Hp
( Fv of axis I.e. center line of view to xy as shown) & project final Tv.

## Slide 75
X
Y
a
d
bo
b’d’ c’
a’
o’
b1 c1
c a1
d1
o1
o’1
a’1
b’1
c’1
d’1
Problem 4:A square pyramid 30 mm base side
and 50 mm long axis is resting on it’s apex on Hp, such that it’s one slant edge is vertical and a triangular face through it is perpendicular to Vp.
Draw it’s projections.
Solution Steps :
1.Assume it standing on Hp but as said on apex.( inverted ). 2.It’s Tv will show True Shape of base( square)
3.Draw a corner case square of 30 mm sides as Tv(as shown) Showing all slant edges dotted, as those will not be visible from top. 4.taking 50 mm axis project Fv. ( a triangle)
Name all points as shown in illustration.
Draw 2nd Fv keeping o’a’ slant edge vertical & project it’s Tv 7.Make visible lines dark and hidden dotted, as per the procedure. 8.Then redrew 2nd Tv as final Tv keeping a1o1d1 triangular face
perpendicular to Vp I.e.xy. Then as usual project final Fv.

## Slide 76
Problem 5: A cube of 50 mm long edges is so placed on Hp on one corner that a body diagonal is parallel to Hp and perpendicular to Vp Draw it’s projections.
X
Y
b
c
d
a
a’
c’
b’d’
a1
b1
d1
c1
1’
a’1
d’1
c’1
d’
1
Solution Steps:
1.Assuming standing on Hp, begin with Tv,a square with all sides equally inclined to xy.Project Fv and name all points of FV & TV. 2.Draw a body-diagonal joining c’ with 3’( This can become // to xy) 3.From 1’ drop a perpendicular on this and name it p’
4.Draw 2nd Fv in which 1’-p’ line is vertical means c’-3’ diagonal must be horizontal. .Now as usual project Tv..
6.In final Tv draw same diagonal is perpendicular to Vp as said in problem. Then as usual project final FV.
1’
3’
1’
3’

## Slide 77
Y
Problem 6:A tetrahedron of 50 mm long edges is resting on one edge on
Hp while one triangular face containing
this edge is vertical and 450 inclined to Vp. Draw projections.
X
T L
a
o
b
c
b’
a’
c’
o’
a1
c1
o1
b1
900
450
c’
1
a’1
o’1
b’1
IMPORTANT:
Tetrahedron is a special type
of triangular pyramid in which base sides & slant edges are equal in length.
Solid of four faces. Like cube it is also described by One dimension only..
Axis length generally not given.
Solution Steps
As it is resting assume it standing on Hp.
Begin with Tv , an equilateral triangle as side case as shown: First project base points of Fv on xy, name those & axis line. From a’ with TL of edge, 50 mm, cut on axis line & mark o’ (as axis is not known, o’ is finalized by slant edge length) Then complete Fv.
In 2nd Fv make face o’b’c’ vertical as said in problem. And like all previous problems solve completely.

## Slide 78
ENGINEERING APPLICATIONS OF
THE PRINCIPLES OF
PROJECTIONS OF SOLIDES.
SECTIONS OF SOLIDS.
DEVELOPMENT.
INTERSECTIONS.
STUDY CAREFULLY
THE ILLUSTRATIONS GIVEN ON NEXT SIX PAGES !

## Slide 79: SECTIONING A SOLID. An object ( here a solid ) is cut by some imaginary cutting plane
The action of cutting is called SECTIONING a solid
&
The plane of cutting is called
SECTION PLANE.
to understand internal details of that object.
Two cutting actions means section planes are recommended.
A) Section Plane perpendicular to Vp and inclined to Hp.
( This is a definition of an Aux. Inclined Plane i.e. A.I.P.)
NOTE:- This section plane appears as a straight line in FV.
B) Section Plane perpendicular to Hp and inclined to Vp.
( This is a definition of an Aux. Vertical Plane i.e. A.V.P.)
NOTE:- This section plane appears
as a straight line in TV.
Remember:-
After launching a section plane
either in FV or TV, the part towards observer is assumed to be removed.
As far as possible the smaller part is
assumed to be removed.
OBSERVER
ASSUME UPPER PART REMOVED
OBSERVER
ASSUME LOWER PART REMOVED
(A)
(B)

## Slide 80: ILLUSTRATION SHOWING IMPORTANT TERMS IN SECTIONING.
y
TRUE SHAPE
Of SECTION
SECTION PLANE
SECTION LINES (450 to XY)
x
Apparent Shape of section
SECTIONAL T.V.
For TV

## Slide 81: Typical Section Planes &
Section Plane Through Generators
Section Plane Parallel to end generator.
Section Plane
Parallel to Axis.
Section PlaneTriangle
Through Apex
Ellipse
Hyperbola
Ellipse
Cylinder through generators.
Sq. Pyramid through all slant edges
Trapezium
Typical Shapes Of
Sections.

## Slide 82: DEVELOPMENT OF SURFACES OF SOLIDS.
MEANING:-
ASSUME OBJECT HOLLOW AND MADE-UP OF THIN SHEET. CUT OPEN IT FROM ONE SIDE AND UNFOLD THE SHEET COMPLETELY. THEN THE SHAPE OF THAT UNFOLDED SHEET IS CALLED DEVELOPMENT OF LATERLAL SUEFACES OF THAT OBJECT OR SOLID.
LATERLAL SURFACE IS THE SURFACE EXCLUDING SOLID’S TOP & BASE.
ENGINEERING APLICATION:
THERE ARE SO MANY PRODUCTS OR OBJECTS WHICH ARE DIFFICULT TO MANUFACTURE BY CONVENTIONAL MANUFACTURING PROCESSES, BECAUSE OF THEIR SHAPES AND SIZES. THOSE ARE FABRICATED IN SHEET METAL INDUSTRY BY USING
DEVELOPMENT TECHNIQUE. THERE IS A VAST RANGE OF SUCH OBJECTS.
EXAMPLES:-
Boiler Shells & chimneys, Pressure Vessels, Shovels, Trays, Boxes & Cartons, Feeding Hoppers,
Large Pipe sections, Body & Parts of automotives, Ships, Aeroplanes and many more.
WHAT IS
OUR OBJECTIVE IN THIS TOPIC ?
To learn methods of development of surfaces of different solids, their sections and frustums.
Development is different drawing than PROJECTIONS.
It is a shape showing AREA, means it’s a 2-D plain drawing.
Hence all dimensions of it must be TRUE dimensions.
As it is representing shape of an un-folded sheet, no edges can remain hidden And hence DOTTED LINES are never shown on development.
But before going ahead, note following Important points.
Study illustrations given on next page carefully.

## Slide 83
D
H
D
S
S
H
 = R
L
3600

R=Base circle radius.
L=Slant height.
L= Slant edge.
S = Edge of base
H= Height
S = Edge of base
H= Height D= base diameter
Development of lateral surfaces of different solids. (Lateral surface is the surface excluding top & base)
Prisms:
No.of Rectangles
Cylinder:
A Rectangle
Cone: (Sector of circle)
Pyramids: (No.of triangles)
Tetrahedron: Four Equilateral Triangles
All sides equal in length
Cube: Six Squares.

## Slide 84: FRUSTUMS

 = R
L
3600
R= Base circle radius of cone L= Slant height of cone
L1 = Slant height of cut part.
Top side
DEVELOPMENT OF
FRUSTUM OF SQUARE PYRAMID
Base side
L= Slant edge of pyramid L1 = Slant edge of cut part.
DEVELOPMENT OF
FRUSTUM OF CONE
STUDY NEXT NINE PROBLEMS OF SECTIONS & DEVELOPMENT

## Slide 85
X
Y
X1
Y
1
A
B
E
D
a
e
d
b
c
A
B
C
D
E
A
DEVELOPMENT
a”
b”
c”
d”
e”
Problem 1: A pentagonal prism , 30 mm base side & 50 mm axis
is standing on Hp on it’s base whose one side is perpendicular to Vp. It is cut by a section plane 450 inclined to Hp, through mid point of axis. Draw Fv, sec.Tv & sec. Side view. Also draw true shape of section and Development of surface of remaining solid.
C
Solution Steps:for sectional views: Draw three views of standing prism. Locate sec.plane in Fv as described. Project points where edges are getting Cut on Tv & Sv as shown in illustration. Join those points in sequence and show Section lines in it.
Make remaining part of solid dark.
For True Shape:
Draw x1y1 // to sec. plane Draw projectors on it from
cut points.
Mark distances of points of Sectioned part from Tv, on above projectors from
x1y1 and join in sequence. Draw section lines in it.
It is required true shape.
For Development:
Draw development of entire solid. Name from cut-open edge I.e. A. in sequence as shown. Mark the cut points on respective edges.
Join them in sequence in st. lines. Make existing parts dev.dark.

## Slide 86
Y
h
a
b
d
e
g
f
X
’ c’ g’
f’ d’ e’
a’ h’b
o’
X1
Y1
g” h”f”
a”e”
b”d” c”
A
B
C
D
E
F
A
G
H
c
SECTIONAL T.V
SECTIONAL S.V
DEVELOPMENT
Problem 2: A cone, 50 mm base diameter and 70 mm axis is standing on it’s base on Hp. It cut by a section plane 450 inclined to Hp through base end of end generator.Draw projections,
sectional views, true shape of section and development of surfaces
of remaining solid.
Solution Steps:for sectional views: Draw three views of standing cone. Locate sec.plane in Fv as described. Project points where generators are getting Cut on Tv & Sv as shown in illustration.Join those points in sequence and show Section lines in it. Make remaining part of solid dark.
For True Shape:
Draw x1y1 // to sec. plane Draw projectors on it from cut points.
Mark distances of points of Sectioned part from Tv, on above projectors from
x1y1 and join in sequence.
Draw section lines in it. It is required true shape.
For Development:
Draw development of entire solid. Name from cut-open edge i.e. A.
in sequence as shown.Mark the cut
points on respective edges.
Join them in sequence in curvature. Make existing parts dev.dark.

## Slide 87
X
Y
c’ g’
f’ d’ e’
a’ h’b’
o’
o’
C
D
E
F
A
G
H
O
DEVELOPMENT
A
B
a1
h1
g1
f1
d1
c
1
b1
o1
SECTIONAL T.V
(SHOWING TRUE SHAPE OF SECTION)
HORIZONTAL SECTION PLANE
h
a
b
c
d
e e1
g
f
O
Problem 3: A cone 40mm diameter and 50 mm axis is resting on one generator on Hp( lying on Hp) which is // to Vp.. Draw it‟s projections.It is cut by a horizontal section plane through it‟s base center. Draw sectional TV, development of the surface of the remaining part of cone.
Follow similar solution steps for Sec.views - True shape – Development as per previous problem!

## Slide 88
A.V.P300 inclined to Vp Through mid-point of axis.
X
Y
1
2
3
4
5
6
7
8
a’ b’
c’ f’
d’ e’
a
b
c
d
e
f
b1 d1
a1 e1
c1
f1
X1
Y1
AS SECTION PLANE IS IN T.V.,
CUT OPEN FROM BOUNDRY EDGE C1 FOR DEVELOPMENT.
C
D
E F A
B
C
DEVELOPMENT
SECTIONAL F.V.
Problem 4: A hexagonal prism. 30 mm base side & 55 mm axis is lying on Hp on it’s rect.face with axis
// to Vp. It is cut by a section plane normal to Hp and
300 inclined to Vp bisecting axis.
Draw sec. Views, true shape & development.
Use similar steps for sec.views & true shape. NOTE: for development, always cut open object from From an edge in the boundary of the view in which sec.plane appears as a line.
Here it is Tv and in boundary, there is c1 edge.Hence it is opened from c and named C,D,E,F,A,B,C.
Note the steps to locate Points 1, 2 , 5, 6 in sec.Fv: Those are transferred to 1st TV, then to 1st Fv and Then on 2nd Fv.

## Slide 89
1’
2’
3’
4’
5’
6’
7’
1
5
4
3
2
6
7
1
6
5
4
3
2
a
b
c
d
e
g
4
4
5
3
6
2
7
1
A
B
C
D
E
A
F
G
O
d’e’
c’f’ f
g’b’ a’
X
Y
X1
Y1
O’
F.V.
SECTIONAL 7
TOP VIEW.
Problem 5:A solid composed of a half-cone and half- hexagonal pyramid is shown in figure.It is cut by a section plane 450 inclined to Hp, passing through mid-point of axis.Draw F.v., sectional T.v.,true shape of section and development of remaining part of the solid.
( take radius of cone and each side of hexagon 30mm long and axis 70mm.)
Note:
Fv & TV 8f two solids sandwiched
Section lines style in both:
Development of
half cone & half pyramid:

## Slide 90: INTERPENETRATION OF SOLIDS
WHEN ONE SOLID PENETRATES ANOTHER SOLID THEN THEIR SURFACES INTERSECT AND
AT THE JUNCTION OF INTERSECTION A TYPICAL CURVE IS FORMED, WHICH REMAINS COMMON TO BOTH SOLIDS.
THIS CURVE IS CALLED CURVE OF INTERSECTION AND
IT IS A RESULT OF INTERPENETRATION OF SOLIDS.
PURPOSE OF DRAWING THESE CURVES:-
WHEN TWO OBJECTS ARE TO BE JOINED TOGATHER, MAXIMUM SURFACE CONTACT BETWEEN BOTH BECOMES A BASIC REQUIREMENT FOR STRONGEST & LEAK-PROOF JOINT.
Curves of Intersections being common to both Intersecting solids, show exact & maximum surface contact of both solids.
Study Following Illustrations Carefully.
Square Pipes.
Circular Pipes.
Square Pipes.
Circular Pipes.
Minimum Surface Contact.
( Point Contact)
(Maximum Surface Contact)
Lines of Intersections. Curves of Intersections.

## Slide 91
A machine component having two intersecting cylindrical surfaces with the axis at acute angle to each other.
Intersection of a Cylindrical main and Branch Pipe.
Pump lid having shape of a
hexagonal Prism and Hemi-sphere intersecting each other.
Forged End of a Connecting Rod.
A Feeding Hopper In industry.
An Industrial Dust collector.
Intersection of two cylinders.
Two Cylindrical surfaces.
SOME ACTUAL OBJECTS ARE SHOWN, SHOWING CURVES OF INTERSECTIONS. BY WHITE ARROWS.

## Slide 92: COMMON SOLUTION STEPS
FOLLOWING CASES ARE SOLVED. REFFER ILLUSTRATIONS
AND
NOTE THE COMMON CONSTRUCTION FOR ALL
1.CYLINDER TO CYLINDER2.
2.SQ.PRISM TO CYLINDER
3.CONE TO CYLINDER
4.TRIANGULAR PRISM TO CYLNDER
5.SQ.PRISM TO SQ.PRISM
SQ.PRISM TO SQ.PRISM ( SKEW POSITION)
SQARE PRISM TO CONE ( from top )
8.CYLINDER TO CONE
One solid will be standing on HP Other will penetrate horizontally. Draw three views of standing solid. Name views as per the illustrations. Beginning with side view draw three Views of penetrating solids also.
On it’s S.V. mark number of points And name those(either letters or nos.) The points which are on standard generators or edges of standing solid, ( in S.V.) can be marked on respective generators in Fv and Tv. And other points from SV should be brought to Tv first and then projecting upward To Fv.
Dark and dotted line’s decision should be taken by observing side view from it’s right side as shown by arrow.
Accordingly those should be joined by curvature or straight lines.
Note:
Incase cone is penetrating solid Side view is not necessary. Similarly in case of penetration from top it is not required.

## Slide 93
X
Y
1
2
3
4
a”
g”
c”
e”
b”
f”
d”
h”
4”
1”3”
1’
2’ 4’
3’
a’
b ’h’
c’g’
d’f’
a’
CASE 1.
CYLINDER STANDING
&
CYLINDER PENETRATING
2”
Problem: A cylinder 50mm dia.and 70mm axis is completely penetrated by another of 40 mm dia.and 70 mm axis horizontally Both axes intersect & bisect each other. Draw projections showing curves of intersections.

## Slide 94
X
Y
a”
d”
b”
c”
1”3”
1’
1
2
3
4
2’ 4’ 3’ 4”
a’
d’
b’
c’
a’
c’
d’
b’
CASE 2.
CYLINDER STANDING
&
SQ.PRISM PENETRATING
2”
Problem: A cylinder 50mm dia.and 70mm axis is completely penetrated by a square prism of 25 mm sides.and 70 mm axis, horizontally. Both axes Intersect & bisect each other. All faces of prism are equally inclined to Hp. Draw projections showing curves of intersections.

## Slide 95: CASE 3.
X
Y
CYLINDER STANDING
&
CONE PENETRATING
Problem: A cylinder of 80 mm diameter and 100 mm axis is completely penetrated by a cone of 80 mm diameter and 120 mm long axis horizontally.Both axes intersect & bisect each other. Draw projections showing curve of intersections.
1
2 8
3 7
4 6
5
7’
6’ 8’
1’ 5’
2’ 4’
3’

## Slide 96
X
Y
a”
d”
b”
c”
a’
c’
a’
d’
b’
c’
d’
b’
1
2
3
4
1’
2’4’
3’
4”
1”3”
2”
CASE 4.
&
SQ.PRISM PENETRATING
Problem: A sq.prism 30 mm base sides.and 70mm axis is completely penetrated
by another square prism of 25 mm sides.and 70 mm axis, horizontally. Both axesSQ.PRISM STANDING
Intersects & bisect each other. All faces of prisms are equally inclined to Vp. Draw projections showing curves of intersections.

## Slide 97
X
Y
1
2
3
4
1’
b
e
1”3” 2”
a
c
d
f
b
b
c
d
e
e
2’4’ 3’ 4”
a
a
f
f
Problem: A cylinder 50mm dia.and 70mm axis is completely penetrated
by a triangular prism of 45 mm sides.and 70 mm axis, horizontally. One flat face of prism is parallel to Vp and Contains axis of cylinder. Draw projections showing curves of intersections.
CASE 5. CYLINDER STANDING & TRIANGULAR PRISM PENETRATING

## Slide 98: CASE 6.
X
Y
1
2
3
4
1’
2’4’ 3’
4”
300
c”
f”
a’
f’
d’
e’
b’
c’
SQ.PRISM STANDING
&
SQ.PRISM PENETRATING (300 SKEW POSITION)
1”3” 2”
Problem: A sq.prism 30 mm base sides.and 70mm axis is completely penetrated by another square prism of 25 mm side s.and 70 mm axis, horizontally. Both axes Intersect & bisect each other.Two faces of penetrating prism are 300 inclined to Hp. Draw projections showing curves of intersections.

## Slide 99: ISOMETRIC DRAWING
H
3-D DRAWINGS CAN BE DRAWN
IN NUMEROUS WAYS AS SHOWN BELOW. ALL THESE DRAWINGS MAY BE CALLED
3-DIMENSIONAL DRAWINGS, OR PHOTOGRAPHIC
OR PICTORIAL DRAWINGS. HERE NO SPECIFIC RELATION
AMONG H, L & D AXES IS MENTAINED.
H
NOW OBSERVE BELOW GIVEN DRAWINGS. ONE CAN NOTE SPECIFIC INCLINATION AMONG H, L & D AXES.
ISO MEANS SAME, SIMILAR OR EQUAL. HERE ONE CAN FIND
EDUAL INCLINATION AMONG H, L & D AXES. EACH IS 1200 INCLINED WITH OTHER TWO. HENCE IT IS CALLED ISOMETRIC DRAWING
H
L
IT IS A TYPE OF PICTORIAL PROJECTION IN WHICH ALL THREE DIMENSIONS OF
AN OBJECT ARE SHOWN IN ONE VIEW AND IF REQUIRED, THEIR ACTUAL SIZES CAN BE MEASURED DIRECTLY FROM IT.
IN THIS 3-D DRAWING OF AN OBJECT, ALL THREE DIMENSIONAL AXES ARE MENTAINED AT EQUAL INCLINATIONS WITH EACH OTHER.( 1200)
PURPOSE OF ISOMETRIC DRAWING IS TO UNDERSTAND
OVERALL SHAPE, SIZE & APPEARANCE OF AN OBJECT PRIOR TO IT‟S PRODUCTION.
TYPICAL CONDITION.

## Slide 100: SOME IMPORTANT TERMS:
ISOMETRIC AXES, LINES AND PLANES:
The three lines AL, AD and AH, meeting at point A and making 1200 angles with each other are termed Isometric Axes.
The lines parallel to these axes are called Isometric Lines.
The planes representing the faces of of the cube as well as other planes parallel to these planes are called Isometric Planes.
ISOMETRIC SCALE:
When one holds the object in such a way that all three dimensions
are visible then in the process all dimensions become proportionally
inclined to observer‟s eye sight and hence appear apparent in lengths.
This reduction is 0.815 or 9 / 11 ( approx.) It forms a reducing scale which Is used to draw isometric drawings and is called Isometric scale.
In practice, while drawing isometric projection, it is necessary to convert true lengths into isometric lengths for measuring and marking the sizes. This is conveniently done by constructing an isometric scale as described on next page.
H
A

## Slide 101
H
H
TYPES OF ISOMETRIC DRAWINGS
ISOMETRIC PROJECTION
Drawn by using Isometric scale
( Reduced dimensions )
ISOMETRIC VIEW
Drawn by using True scale ( True dimensions )
450
1
2
3
0
0 300
1
2
3
Isometric scale [ Line AC ] required for Isometric Projection
A
B
C
4
D
4
CONSTRUCTION OF ISOM.SCALE.
From point A, with line AB draw 300 and 450 inclined lines AC & AD resp on AD. Mark divisions of true length and from each division-point draw vertical lines upto AC line.
The divisions thus obtained on AC give lengths on isometric scale.

## Slide 102: Isometric view if the Shape is
SHAPE
TRIANGLE
A
B
RECTANGLE
D
C
H
F.V. or T.V.
D
A
B
C
A
B
D
C
H
1
2
3
A
B
3
1
2
A
B
3
1
2
A
B
H
1
2
3
4
A
B
C
D
PENTAGON
E
1
2
3
4
A
B
C
D
E
1
2
3
4
A
B
C
D
E
ISOMETRIC
OF PLANE FIGURES
AS THESE ALL ARE 2-D FIGURES
WE REQUIRE ONLY TWO ISOMETRIC AXES.
IF THE FIGURE IS FRONT VIEW, H & L AXES ARE REQUIRED.
IF THE FIGURE IS TOP VIEW, D & L AXES ARE REQUIRED.
Shapes containing Inclined lines should be enclosed in a rectangle as shown.
Then first draw isom. of that rectangle and then inscribe that shape as it is.
1

## Slide 103: STUZDY
1
4
3
A
B
D
C
ILLUSTRATIONS
DRAW ISOMETRIC VIEW OF A CIRCLE IF IT IS A TV OR FV.
FIRST ENCLOSE IT IN A SQUARE.
IT‟S ISOMETRIC IS A RHOMBUS WITH D & L AXES FOR TOP VIEW.
THEN USE H & L AXES FOR ISOMETRIC WHEN IT IS FRONT VIEW.
FOR CONSTRUCTION USE RHOMBUS METHOD SHOWN HERE. STUDY IT.
2
2

## Slide 104: STUZDY
100 MM
IF TOP VIEW
50 MM
ILLUSTRATIONS
25 R
DRAW ISOMETRIC VIEW OF THE FIGURE SHOWN WITH DIMENTIONS (ON RIGHT SIDE) CONSIDERING IT FIRST AS F.V. AND THEN T.V.
IF FRONT VIEW
3

## Slide 105: SHAPE
CIRCLE
HEXAGON
ISOMETRIC
OF PLANE FIGURES
AS THESE ALL ARE 2-D FIGURES
WE REQUIRE ONLY TWO ISOMETRIC AXES.
IF THE FIGURE IS FRONT VIEW, H & L AXES ARE REQUIRED.
IF THE FIGURE IS TOP VIEW, D & L AXES ARE REQUIRED.
IF F.V.
IF T.V.
For Isometric of Circle/Semicircle use Rhombus method. Construct Rhombus of sides equal to Diameter of circle always. ( Ref. topic ENGG. CURVES.)
SEMI CIRCLE
For Isometric of
Circle/Semicircle use Rhombus method.
Construct it of sides equal to diameter of circle always. ( Ref. Previous two pages.)
4

## Slide 106: STUDY
1
3
4
A
B
2
C
D
E
1
2
3
4
A
B
C
D
E
ISOMETRIC VIEW OF PENTAGONAL PYRAMID STANDING ON H.P.
(Height is added from center of pentagon)
ISOMETRIC VIEW OF BASE OF PENTAGONAL PYRAMID STANDING ON H.P.
ILLUSTRZATIONS
5

## Slide 107: STUDY
H
1
2
4
A
B
3
C
D
E
ILLUSTRZATIONS
ISOMETRIC VIEW OF PENTAGONALL PRISM LYING ON H.P.
ISOMETRIC VIEW OF HEXAGONAL PRISM STANDING ON H.P.
6

## Slide 108: ILLUSTRZATIONS
STUDY
CYLINDER LYING ON H.P.
CYLINDER STANDING ON H.P.
7

## Slide 109
STUDY
ILLUSTRZATIONS
HALF CYLINDER
LYING ON H.P.
( with flat face // to H.P.)
HALF CYLINDER
STANDING ON H.P.
( ON IT’S SEMICIRCULAR BASE)
8

## Slide 110
STUDY
ILLUSTRZATIONS
ISOMETRIC VIEW OF
A FRUSTOM OF SQUARE PYRAMID
STANDING ON H.P. ON IT’S LARGER BASE.
40 20
60
X
Y
FV
TV
9

## Slide 111: STUDY ILLUSTRATION
ISOMETRIC VIEW OF
FRUSTOM OF PENTAGONAL PYRAMID
1
3
4
y
A
B
2
C
D
E
40
20
60
x
FV
TV
PROJECTIONS OF FRUSTOM OF PENTAGONAL PYRAMID ARE GIVEN. DRAW IT‟S ISOMETRIC VIEW.
SOLUTION STEPS:
FIRST DRAW ISOMETRIC OF IT‟S BASE.
THEN DRAWSAME SHAPE AS TOP, 60 MM ABOVE THE BASE PENTAGON CENTER.
THEN REDUCE THE TOP TO 20 MM SIDES AND JOIN WITH
THE PROPER BASE CORNERS.
10

## Slide 112
STUDY
ILLUSTRZATIONS
ISOMETRIC VIEW OF
A FRUSTOM OF CONE
STANDING ON H.P. ON IT’S LARGER BASE.
FV
TV
40 20
60
X
Y
11

## Slide 113
STUDY
ILLUSTRZATIONS
PROBLEM: A SQUARE PYRAMID OF 30 MM BASE SIDES AND 50 MM LONG AXIS, IS CENTRALLY PLACED ON THE TOP OF A
CUBE OF 50 MM LONG EDGES.DRAW ISOMETRIC VIEW OF THE PAIR.
12

## Slide 114: STUDY
a
b
o c
p
p
a
b
c
o
ILLUSTRZATIONS
PROBLEM: A TRIANGULAR PYRAMID OF 30 MM BASE SIDES AND 50 MM LONG AXIS, IS CENTRALLY PLACED ON THE TOP OF A CUBE OF 50 MM LONG EDGES.
DRAW ISOMETRIC VIEW OF THE PAIR.
SOLUTION HINTS.
TO DRAW ISOMETRIC OF A CUBE IS SIMPLE. DRAW IT AS USUAL.
BUT FOR PYRAMID AS IT’S BASE IS AN EQUILATERAL TRIANGLE, IT CAN NOT BE DRAWN DIRECTLY.SUPPORT OF IT’S TV IS REQUIRED.
SO DRAW TRIANGLE AS A TV, SEPARATELY AND NAME VARIOUS POINTS AS SHOWN. AFTER THIS PLACE IT ON THE TOP OF CUBE AS SHOWN.
THEN ADD HEIGHT FROM IT’S CENTER AND COMPLETE IT’S ISOMETRIC AS SHOWN.
13

## Slide 115: STUDY
ILLUSTRZATIONS
50
50
TV
30 D
10
30
30
+
FV
PROBLEM:
A SQUARE PLATE IS PIERCED THROUGH CENTRALLY
BY A CYLINDER WHICH COMES OUT EQUALLY FROM BOTH FACES
OF PLATE. IT‟S FV & TV ARE SHOWN. DRAW ISOMETRIC VIEW.
14

## Slide 116: STUDY
ILLUSTRZATIONS
10
30
30
60 D
40 SQUARE
FV
TV
PROBLEM:
A CIRCULAR PLATE IS PIERCED THROUGH CENTRALLY
BY A SQUARE PYRAMID WHICH COMES OUT EQUALLY FROM BOTH FACES OF PLATE. IT‟S FV & TV ARE SHOWN. DRAW ISOMETRIC VIEW.
15

## Slide 117: STUDY
ILLUSTRZATIONS
X
Y
30 D
50 D
10
20
40
FV
40
TV
F.V. & T.V. of an object are given. Draw it‟s isometric view.
16

## Slide 118: ILLUSTZRATIONS ISOMETRIC PROJECTIONS OF SPHERE & HEMISPHERE
P
r
R
R
r
P
C
C = Center of Sphere. P = Point of contact
R = True Radius of Sphere r = Isometric Radius.
R
r
P
r
R
C
r
r
450
300
TO DRAW ISOMETRIC PROJECTION OF A HEMISPHERE
TO DRAW ISOMETRIC PROJECTION OF A SPHERE
FIRST DRAW ISOMETRIC OF SQUARE PLATE.
LOCATE IT‟S CENTER. NAME IT P.
FROM PDRAW VERTICAL LINE UPWARD, LENGTH „ r mm‟ AND LOCATE CENTER OF SPHERE “C”
„C‟ AS CENTER, WITH RADIUS „R‟ DRAW CIRCLE.
THIS IS ISOMETRIC PROJECTION OF A SPHERE.
Adopt same procedure.
Draw lower semicircle only. Then around „C‟ construct Rhombus of Sides equal to Isometric Diameter.
For this use iso-scale. Then construct ellipse in this Rhombus as usual And Complete
Isometric-Projection of Hemi-sphere.
STUDY
Isom. Scale
17

## Slide 119: STUZDY
P
r
R
r
r
50 D
30 D
50
450
300
PROBLEM:
A HEMI-SPHERE IS CENTRALLY PLACED ON THE TOP OF A FRUSTOM OF CONE.
DRAW ISOMETRIC PROJECTIONS OF THE ASSEMBLY.
50 D
FIRST CONSTRUCT ISOMETRIC SCALE. USE THIS SCALE FOR ALL DIMENSIONS IN THIS PROBLEM.
ILLUSTRATIONS
18

## Slide 120: STUDY
a
b
c
d
1
2
3
4
o
3’ 4’
1’2’
1
2
4
3
X
Y
ILLUSTRZATIONS
A SQUARE PYRAMID OF 40 MM BASE SIDES AND 60 MM AXIS
IS CUT BY AN INCLINED SECTION PLANE THROUGH THE MID POINT
OF AXIS AS SHOWN.DRAW ISOMETRIC VIEW OF SECTION OF PYRAMID.
19

## Slide 121: STUDY
ILLUSTRZATIONS
Y
50
20
25
25
20
X O
O
F.V. & T.V. of an object are given. Draw it‟s isometric view.
20

## Slide 122: STUDY
ILLUSTRZATIONS
x
FV
TV
35
35
10 y
20 30
10
40
70
O
O
F.V. & T.V. of an object are given. Draw it‟s isometric view.
21